## Slide 1: Generation of Mixed-Driving Multi-Bit Flip-Flops for Power Optimization
Meng-Yun Liu, Yu-Cheng Lai, Wai-Kei Mak, and Ting-Chi Wang
Department of Computer Science, National Tsing Hua University
Hsinchu, Taiwan

## Slide 2: Outline
Introduction
Problem Formulation
Proposed Approach
  Compute Feasible Regions of FFs
  Find All Maximal Cliques in Multiple Rectangle Intersection Graphs
  Non-Conflicting MBFFs Generation
  Location Assignment
  Timing-Driven MBFF Sizing
Experimental Result

## Slide 3: Outline
Introduction
Problem Formulation
Proposed Approach
  Compute Feasible Regions of FFs
  Find All Maximal Cliques in Multiple Rectangle Intersection Graphs
  Non-Conflicting MBFFs Generation
  Location Assignment
  Timing-Driven MBFF Sizing
Experimental Result

## Slide 4: Introduction
Clock network accounts for a major portion of power consumption in a chip
MBFFs can reduce the clock network usage, thus it is often used in low-power circuit design. The reasons are:
  The power per bit for an MBFF is smaller than a single-bit FF
  Using MBFFs reduces the number of clock sinks, resulting in less clock power consumption
    Greatly reduces the wirelength of the clock tree
    Greatly reduces the clock buffer count
Mixed-driven MBFF will have smaller area than uniform-driven MBFF

## Slide 5: Introduction
Multi-bit flip-flops (MBFFs) often used to reduce the number of clock sinks, which results in a low power design
“Traditional MBFF” is composed of individual FFs of uniform driving strength
  If some but not all of the of an MBFF violate timing constraints, the MBFF has to be sized up to a higher driving strength or decomposed into smaller bit-width combinations to satisfy timing, which reduces the power saving
This paper present a “new MBFF”, which certain bits have a higher driving strength than the other bits
  To maximize the FF merging rate, they perform aggressive FF merging subject to timing constraints
  Willing to possibly oversize some FFs, and allow the presence of empty bits in MBFF, which is for merging FFs into MBFF’s uniform driven strength as much as possible
  The oversized FF of the MBFF will be downsized subject to timing constraint with latter approach

## Slide 6: Introduction

## Slide 7: Introduction

## Slide 8: Outline
Introduction
Problem Formulation
Proposed Approach
  Compute Feasible Regions of FFs
  Find All Maximal Cliques in Multiple Rectangle Intersection Graphs
  Non-Conflicting MBFFs Generation
  Location Assignment
  Timing-Driven MBFF Sizing
Experimental Result

## Slide 9: Problem Formulation
An MBFF library containing uniform-driving and mixed-driving MBFFs, where the driving strength is from 1x to 𝑛x and the amount of bits is from 2 to 𝑘, is adopted
The Mixed-Driving MBFF Generation Problem is defined as follows:
  Input
    A netlist
    An associated legal placement
    If there are uniform-driving MBFFs in the design, they will be pre-processed by decomposing them into multiple single-bit FFs while keeping the driving strengths intact
  Output
    A refined netlist containing mixed-driving MBFFs
    A refined placement without timing violations
The objective is to minimize the amount of oversized MBFFs for power optimization, resulting in a low-power design

## Slide 10: Problem Formulation

## Slide 11: Outline
Introduction
Problem Formulation
Proposed Approach
  Compute Feasible Regions of FFs
  Find All Maximal Cliques in Multiple Rectangle Intersection Graphs
  Non-Conflicting MBFFs Generation
  Location Assignment
  Timing-Driven MBFF Sizing
Experimental Result

## Slide 12: Compute Feasible Regions of FFs
To obtain a mixed-driving MBFF design for maximum power reduction under timing constraints, the key idea is to allow upsizing of the original individual FFs to increase their merging choices when forming the MBFFs, then at the end downsizing some bits in the MBFFs formed after placement legalization while preserving timing

## Slide 13: Compute Feasible Regions of FFs
Obtain the fan-in/fan-out pin locations and their timing slacks of original FF in the design under different driving strengths
Compute the timing feasible regions of each FF under different driving strengths
The maximal cliques in each rectangle intersection graph corresponding to maximal groups of FFs that can be merged without timing violations are found to facilitate the generation of potential MBFFs

## Slide 14: Compute Feasible Regions of FFs
Obtain the fan-in/fan-out pin locations and their timing slacks of original FF in the design under different driving strengths
Compute the timing feasible regions of each FF under different driving strengths
The maximal cliques in each rectangle intersection graph corresponding to maximal groups of FFs that can be merged without timing violations are found to facilitate the generation of potential MBFFs

## Slide 16
Thank You for Listening!