## Slide 1: Stronger Mixed-Size Placement Backbone Considering Second-Order Information
Yifan Chen, Zaiwen Wen, Yun Liang, Yibo Lin
Peking University, China
Presenter : Min-Feng Hsieh
Adviser : Ting-Chi Wang
Notes: 上海鐳達晶元智慧科技有限公司
復旦大學專用積體電路與系統國家重點實驗室

## Slide 2: Outline
Abstract
Introduction
Preliminaries
Proposed Algorithm
  Congestion Estimation
  Cell Padding
  Strategy Exploration
  Legalization
Experimental Result

## Slide 3: Introduction
Macro placement significantly effects the eventual quality of the placement result.
Existing analytical placement algorithm may fail if the parameter is not well-tuned.
Some mixed-size placement algorithms leverage mathematical optimization.
  mPL6, NTUplace, ePlace-MS
Some research focuses on efficient data structures to represent a macro placement.
  CG, MP-tree, CP-tree

## Slide 4: Introduction
Some machine learning techniques have also been proposed.
  Macro placement solutions based on routability prediction.
  Graph learning based initialization for mixed-size placement.
  Reinforcement learning for macro refinement.
AutoDMP apply DREAMPlace to performs hyper-parameter searching upon a mixed-size placement.
  Considering the congestion and the WL.

## Slide 5: Introduction
The macros’ motion will cause drastic changes in the gradient due to their heterogeneous sizes.
  Most mixed-size placement algorithms rely on first-order gradient information
They aim to address the convergence issue by considering second-order

## Slide 6: Outline
Abstract
Introduction
Preliminaries
Proposed Algorithm
  Congestion Estimation
  Cell Padding
  Strategy Exploration
  Legalization
Experimental Result

## Slide 7
  Including three stages:
    Global placement
    Legalization
    Detail placement
Preliminaries - Analytical Mixed-Size Placement
Notes: GR: 將instance分散到layout中
Legalization: 將instance中的overlap消除並且進行alignment
DR: further improve the quality

## Slide 8: Preliminaries - Analytical Mixed-Size Placement
We can formulate analytical global routing problem as:
weight of net e
wirelength
Density penalty to spread cells
λ : Density penalty factor

## Slide 9: Preliminaries – Macro Legalzation
Legalization stage will ensure non-overlapping with minimum displacement.
The legalization will be divided into two parts:
  Macro legalization
  Instance legalization
Mainly focus on macro legalization in this paper.
Notes: Electrostatic: 靜電
𝑊_(𝑒_𝑖 ) (𝑥, 𝑦): weighted wirelength of net ei
Γ: smoothing parameter used to adjust the accuracy.

## Slide 10: Preliminaries – Macro Legalization
Macro legalization can be formulated as following.
() The coordinates before legalization
(): The width and height of the instance i
the left (right) boundary of the layout
: the bottom (top) boundary of the layout
Notes: Electrostatic: 靜電
𝑊_(𝑒_𝑖 ) (𝑥, 𝑦): weighted wirelength of net ei
Γ: smoothing parameter used to adjust the accuracy.

## Slide 11: Preliminaries – Sequence Pair
Many works have focused on efficiently generating a legal layout from a given sequence pair.
In macro legalization, converting a placement with overlaps to a sequence pair can be done in .
  With cutting-based overlap removal and sweep line algorithm.
Check if a sequence pair is legal in
  With longest common sub-sequence algorithm.

## Slide 12: Algorithm
GR: use Barzilai-Borwein method enabled Nesterov algorithm to solve the mixed-sized analytical GR problem.
Legalization: Their legalization method to remove overlap between the macros toward minimum displacement.
Restart GR: Fix the macro and scale down the density penalty weight , and only movable cells can be moved from its current position.

## Slide 13: Algorithm

## Slide 14
Thank you for listening!