## Slide 1: PUFFER :A Routability-Driven Placement Framework via Cell Padding
Yao-Wen Chang
Department of Electrical Engineering
National Taiwan University, Taipei 10617, Taiwan
Zhijie Cai, Peng Zou, Xingyu Tong, Jun Yu, Jianli Chen
State Key Lab of ASIC & System
Fudan University, Shanghai 200433, China
Zhengtao Wu
Shanghai LEDA Technology Co., Ltd.,
Shanghai 201203, China
Presenter : Min-Feng Hsieh
Adviser : Ting-Chi Wang

## Slide 2: Outline
Abstract
Introduction
Preliminaries
Proposed Algorithm
  Congestion Estimation
  Cell Padding
  Strategy Exploration
  Legalization
Experimental Result

## Slide 3: Outline
Abstract
Introduction
Preliminaries
Proposed Algorithm
  Congestion Estimation
  Cell Padding
  Strategy Exploration
  Legalization
Experimental Result

## Slide 4: Abstract
Estimate the congestion by imitating routing detour and clustered cell spreading.
Use the method of cell padding and strategy exploration for optimizing routibility during global placement and legalization stage.
Cell padding considers multiple features, which accumulating accurate congestion.
Apply Bayesian-based method to avoid parameter tuning.
PUFFER achieves best routability with 2.7x(commercial) and 1.4x(Replace) speedups.
Notes: Placement is critical for the routability optimization.

## Slide 5: Outline
Abstract
Introduction
Preliminaries
Proposed Algorithm
  Congestion Estimation
  Cell Padding
  Strategy Exploration
  Legalization
Experimental Result

## Slide 6: Introduction
Routability-driven placement typically consists of:
  Basic placement engine:
    Quadratic placement.
    Non-linear placement.
  Routability optimizer.
    Congestion map, which is generated by probabilistic model [2], [8], [9], [10], [11].
    Integrated global router [3], [4], [5].
    Machine learning based technique [6], [7].
Notes: In quadratic placement, an iterative framework with lower and upper bounds is often applied. The lower bound is described by a quadratic wirelength model to minimize wirelength, and the upper bound is generated by spreading cells in high density regions to remove cell overlaps
In non-linear placement, the objective function is formulated by a non-linear wirelength model subject to a density constraint. By relaxing the density constraint into the objective function, the placement problem can be solved by gradient-descent-based methods to obtain a high-quality placement solution with the desired tradeoff between wirelength and cell density.

## Slide 7: Introduction
Congestion map
  Spread cells in congested regions by cell inflation and rough legalization.
    POLAR 2.0 [8]
    Ripple 2.0 [9]
  White space allocation [10], [11].
  To modify the congestion constraint according to the congestion information [4].
  Modeling routing demands or congestion as a new optimizing target and integrating it into the objective function [13].
Notes: In quadratic placement, an iterative framework with lower and upper bounds is often applied. The lower bound is described by a quadratic wirelength model to minimize wirelength, and the upper bound is generated by spreading cells in high density regions to remove cell overlaps
In non-linear placement, the objective function is formulated by a non-linear wirelength model subject to a density constraint. By relaxing the density constraint into the objective function, the placement problem can be solved by gradient-descent-based methods to obtain a high-quality placement solution with the desired tradeoff between wirelength and cell density.

## Slide 8: Outline
Abstract
Introduction
Preliminaries
Proposed Algorithm
  Congestion Estimation
  Cell Padding
  Strategy Exploration
  Legalization
Experimental Result

## Slide 9: Preliminaries
Routability-driven Placement Problem
Netlist H= (V, E), where V= ,E= .
The placement solution: (x, y) = , where () is the coordinate of .
Routability-driven placer determines legal locations for all movable cells to minimize the routing wirelength and overflow.
Notes: V:cell instance
E: net

## Slide 10: Preliminaries
We can formulate analytical global routing problem as:
wirelength.
Density penalty to spread cells.
λ : Density penalty factor
Notes: Λ : to balance the weight between wirelength and density
* * * * * After doing global routing, we need to legalize the cell positions to remove cell overlaps and DRC violations.

## Slide 11: Preliminaries
Electrostatic-based Placement
This model adopts the weighted-average(WA) wirelength model to approximate the HPWL.
= -
: weighted wirelength of net .
γ : smoothing parameter used to adjust the accuracy.
: the x-coordinate.
Notes: Electrostatic: 靜電
weighted wirelength of net ei
Γ: smoothing parameter used to adjust the accuracy.
Electrostatic: 靜電
𝑊_(𝑒_𝑖 ) (𝑥, 𝑦): weighted wirelength of net ei
Γ: smoothing parameter used to adjust the accuracy.

## Slide 12: Preliminaries
To get the density penalty, the placement region will first divide into uniform bins by M×M grids.
: area of cell i
: the bin in row m and column n
) : the electric potential of

## Slide 13: Preliminaries
Global routing congestion
Use the Gcell-based routing resource model, which evaluates the routing capacity and demand with respect to the Gcell.
=
: the routing demands of Gcell g
: the routing capacity of Gcell g
Notes: Electrostatic: 靜電
𝑊_(𝑒_𝑖 ) (𝑥, 𝑦): weighted wirelength of net ei
Γ: smoothing parameter used to adjust the accuracy.

## Slide 14: Outline
Abstract
Introduction
Preliminaries
Proposed Algorithm
  Congestion Estimation
  Cell Padding
  Strategy Exploration
  Legalization
Experimental Result

## Slide 15: Proposed Algorithm
Notes: Global placement: 用一些placement engine來spread cells 並且 optimize wirelength
Routability optimizer: 會分析現在的congestion information並且利用cell padding來降低congestion
Legalization: 會消除DRC跟overlap

## Slide 16: Outline
Abstract
Introduction
Preliminaries
Proposed Algorithm
  Congestion Estimation
  Cell Padding
  Strategy Exploration
  Legalization
Experimental Result

## Slide 17
Cells in global placement tend to form bunches of clusters since the placement region is divided into bins by a grid.
Cells in the same grid often overlap severely.
Precise routing solution at this stage less meaningful as the overlapped cells inevitably lead to high routing demand.
Congestion Estimation

## Slide 18: Congestion Estimation
Blockage-aware Routing Capacity Assessment (to estimate routing capacity)
Use a Gcell-based routing resource model, which evaluates routing capacity and demand with respect to Gcells.
Routing capacity includes 1. basic capacity and 2. blocked capacity.
  Basic capacity: obtain from tech information (wire width and space).
  Blocked capacity: includes pin obstructions, power ground, macros…
=
Notes: 目的是要找到routing的capacity
CapH=V (g) : the horizontal or vertical routing capacity of Gcell g
l.pd : the preferred routing direction of metal layer l
L : the set of metal layers
Blk : the set of blockages
OLH=V (b; g) is the horizontal or vertical overlaps between blockage b and Gcell g
b.l : the metal layer where the obstacle is located

## Slide 19: Congestion Estimation
Topology-based Congestion Estimation (to estimate the routing demand)
Use FLUTE to get the RSMT topology of the nets, which divide multi-pin net into two-pin net.

## Slide 20: Congestion Estimation
Routing detour-imitating Routing Demand Expansion

## Slide 21: Outline
Abstract
Introduction
Preliminaries
Proposed Algorithm
  Congestion Estimation
  Cell Padding
  Strategy Exploration
  Legalization
Experimental Result

## Slide 22: Cell Padding
CNN and GNN-inspired feature extraction
  Traditional local information – local congestion
=
: the local congestion of cell c
): the congestion of Gcell g
Notes: LCg(c) is the local congestion of cell c
Pos(c) is the Gcell set including all Gcells overlapped with cell c
Cg(g) is the congestion of Gcell g
Cg H/V (g) : horizontal and vertical congestion
Pin density could be calculated by the number of cell pins in each Gcell divided by the number of available sites in each Gcell.

## Slide 23: Cell Padding
CNN and GNN-inspired feature extraction
  Traditional local information – local congestion
=
: the Gcell set including all Gcells overlapped with cell c
horizontal and vertical congestion
Notes: LCg(c) is the local congestion of cell c
Pos(c) is the Gcell set including all Gcells overlapped with cell c
Cg(g) is the congestion of Gcell g
Cg H/V (g) : horizontal and vertical congestion
Pin density could be calculated by the number of cell pins in each Gcell divided by the number of available sites in each Gcell.

## Slide 24: Cell Padding
CNN and GNN-inspired feature extraction
  Traditional local information – pin density
  Pin density =
Notes: LCg(c) is the local congestion of cell c
Pos(c) is the Gcell set including all Gcells overlapped with cell c
Cg(g) is the congestion of Gcell g
Cg H/V (g) : horizontal and vertical congestion
Pin density could be calculated by the number of cell pins in each Gcell divided by the number of available sites in each Gcell.

## Slide 25: Cell Padding
Surrounding congestion and surrounding pin density (CNN)
  To expand a cell’s bounding box vertically and horizontally.
  The size of the expanded bounding box equals to the convolution kernel size.
  The kernel does the mean filter operation.
Notes: Cnn在做convolution的時候，kernel 會提取附近的特徵。所以在這邊他會提取附近的congestion跟pin density

## Slide 26: Cell Padding
Pin congestion to each cell (GNN)
  Could aggregate information from the graph structure in the routing topology.
=
=
𝑃𝐶𝑔(𝑐): Pin congestion of cell c
𝐶𝑔(𝑔): the congestion of Gcell g
Notes: Pin p 的congestion會等於所有p會經過的path l 中該path l(所有跟pin p有關的two point net)有最大gcells congestion的最小值

## Slide 27: Cell Padding
Multi-feature-based Cell Padding
After collecting all the required features, we can calculate the expected padding value.
: the weight of the th feature
β and μ: the strategy parameter
F: the set of features (|F| : total number of features)
Notes: The logarithmic function 是為了要平滑 padding values的distribution, 進而改善padding process的stability
他的strategy parameter會利用一個方法來找，後面會說到

## Slide 28: Cell Padding
Padding Recycling and Utilization Control
Utilize incremental padding strategy which is based on the preceding result.
Recycling rate:
: number of times cell has been padding
: strategy parameter determining the recycling rate

## Slide 29: Cell Padding
Multi-feature-based Cell Padding
If a cell have non-positive padding, it should go through the recycling process to withdraw a part of history padding.
Padding utilization:
: padding utilization of line 5
: strategy parameter determining min and max padding utilization
ξ : max iteration of routing optimization
Notes: 因為這樣可以避免一些可能會增加wirelength的padding

## Slide 30: Cell Padding
Multi-feature-based Cell Padding
Routabililty optimization process:
Notes: 因為這樣可以避免一些可能會增加wirelength的padding
1. 估計congestion
2. 從congestion map跟placement information來提取之前講到的3個features
3、4 : 根據剛剛講到的公式來計算跟回收padding
5: 計算padding utilization (控制padding utilization可以避免Over padding, 阻礙後續的優化)
6-9 : 若total padding超過了設定的utilization,那padding會進行縮放來達到constraint

## Slide 31: Cell Padding
Multi-feature-based Cell Padding
Three conditions to trigger the routability optimizer (, , are strategy parameter) :
  Density flow < threshold
    Density flow:
  Padding utilization of the preceding round < threshold
    Padding is converging
  Call time of routability optimizer < maximum iteration
Otherwise, the WL-driven placement engine will optimize both wirelength and density until it converges.

## Slide 32: Outline
Abstract
Introduction
Preliminaries
Proposed Algorithm
  Congestion Estimation
  Cell Padding
  Strategy Exploration
  Legalization
Experimental Result

## Slide 33: Strategy Exploration
Bayesian-based Strategy Exploration
  In previous stage, several strategy parameter should be determined.
  Placement can be considered as an evaluation-expensive black-box derivative-free
  process
  Apply the sequential model-based global optimization (SMBO) with the tree-
  structured Parzen estimator (TPE) approach [17]

## Slide 34: Strategy Exploration
Bayesian-based Strategy Exploration
Notes: 這個algorithm 2 是有關於parameter exploration
Npc: 結果沒有improve的次數， Tc: 現在執行的iteration數
Parameter list 是給discrete的參數的，parameter range是給continuous的參數的

## Slide 35: Strategy Exploration
Bayesian-based Strategy Exploration
Notes: 這個algorithm3 是有關於他們strategy exploration的計畫，包含兩個部分: 1. global exploration跟2. local exploration
1-2 : 先給定所有parameter一個range，接著所有參數一起跑剛剛講的parameter exploration
3: 接著會將parameters分組，有強相關的會分再一起
6-11: 接著會將分組過後的進行parameter exploration，而不屬於該組的parameters的就會用他們自己range的中位數
當全部跑完後(可以平行)就會得到所有paramete最後的range，接著該parameter就會用那個range的中位數當作最後的值

## Slide 36: Outline
Abstract
Introduction
Preliminaries
Proposed Algorithm
  Congestion Estimation
  Cell Padding
  Strategy Exploration
  Legalization
Experimental Result

## Slide 37: Legalization
White-space-assisted Legalization
  After global placement, we need to place the cell in legal position to eliminate overlaps and DRVs.
  Cells of the same cluster will cling together, degrading routability.
  Inherit the padding from global placement to introduce white space in the congested region.
  To control the padding utilization, we limit the total padding area to less than 5% of the total movable cells area.
  After adding the cell padding, they employ Abacus-based algorithm for legalization.
Notes: 如果total padding超過Limit的話，他們會在discrete padding中挑最小的的padding來釋放他，直到meet constraint

## Slide 38: Legalization
White-space-assisted Legalization
  Width of a cell should be the multiple of the technology site in legalization, So we discretize the padding using a staircase function defined as follows:
  : discrete padding of cell
  strategy parameter
  : maximum padding of all cells
Notes: 這個algorithm3 是有關於他們strategy exploration的計畫，包含兩個部分: 1. global exploration跟2. local exploration
1-2 : 先給定所有parameter一個range，接著所有參數一起跑剛剛講的parameter exploration
3: 接著會將parameters分組，有強相關的會分再一起
6-11: 接著會將分組過後的進行parameter exploration，而不屬於該組的parameters的就會用他們自己range的中位數
當全部跑完後(可以平行)就會得到所有paramete最後的range，接著該parameter就會用那個range的中位數當作最後的值

## Slide 39: Outline
Abstract
Introduction
Preliminaries
Proposed Algorithm
  Congestion Estimation
  Cell Padding
  Strategy Exploration
  Legalization
Experimental Result

## Slide 40: Experimental Result
Environments
  C++ language.
  64-bit CentOS Linux .
  Intel® Xeon(R) Platinum 8260 CPU @ 2.4GHz , using 8 thread.
Benchmarks
Notes: 這個algorithm3 是有關於他們strategy exploration的計畫，包含兩個部分: 1. global exploration跟2. local exploration
1-2 : 先給定所有parameter一個range，接著所有參數一起跑剛剛講的parameter exploration
3: 接著會將parameters分組，有強相關的會分再一起
6-11: 接著會將分組過後的進行parameter exploration，而不屬於該組的parameters的就會用他們自己range的中位數
當全部跑完後(可以平行)就會得到所有paramete最後的range，接著該parameter就會用那個range的中位數當作最後的值

## Slide 41: Experimental Result
They compare their proposed framework PUFFER with RePlAce.
Utilize the global router of Innovus to evaluate the routability of the placememt result.
They take 1% overflow as the pass criterion for routability.
Notes: 因為1%-2%在後續的優化可以修掉

## Slide 42: Experimental Result
HOF : routing overflow ratio of horizontal direction
VOF : routing overflow ratio of vertical direction
WL : global routing wirelength
RT : runtime
2.7x
1.4x
1.045x
Notes: 這個algorithm3 是有關於他們strategy exploration的計畫，包含兩個部分: 1. global exploration跟2. local exploration
1-2 : 先給定所有parameter一個range，接著所有參數一起跑剛剛講的parameter exploration
3: 接著會將parameters分組，有強相關的會分再一起
6-11: 接著會將分組過後的進行parameter exploration，而不屬於該組的parameters的就會用他們自己range的中位數
當全部跑完後(可以平行)就會得到所有paramete最後的range，接著該parameter就會用那個range的中位數當作最後的值

## Slide 43: Experimental Result
Notes: Horizontal congestion map

## Slide 44: Experimental Result
Notes: Vertical congestion map

## Slide 45
Thank you for listening!