## Slide 1: Power Sub-Mesh Construction in Multiple Power Domain Design
Chien-Pang Lu, Iris Hui-Ru Jiang, Chung-Ching Peng, Mohd Razha Mohd Mawardi, Uber Akessandro
Intel Cooperation
National Taiwan University
Presenter : Min-Feng Hsieh
Advisor : Ting-Chi Wang

## Slide 2: Outline
Introduction
Preliminaries
Methodology
Experimental Results

## Slide 3: Introduction
Primary / secondary power mesh : high / low layer stripe.
Multiple power domain design is prevalent for achieving aggressive power savings
Power delivery to cross-domain cells poses a tough challenge at advanced technology nodes.
  IR drop constraint
  Routing source competition between the secondary power routing and regular signal routing.
Explore power sub-mesh construction to mitigate the IR drop issue for cross-domain cells and minimize its routing overhead.
the routing between the secondary power pins on cross-domain cells and power sources

## Slide 4: Introduction
Primary power mesh occupies high layers
  High layer vias are relatively large at advanced technology nodes.
  Each of its stripes can offer a limited number of tapping vias.
If a secondary power pin is not tapped to the nearest power stripe due to limited tapping vias or local congestion.
  It will take a long connection to a distant stripe and in turn induce a severe IR drop due to high resistance.
Notes: 他們現在遇到的問題

## Slide 5: Introduction
To resolve the issue, a local power sub-mesh can be constructed on lower layers.
  Provides smaller and more tapping vias.
  Avoids long connections and maintains low resistance.

## Slide 6: Introduction
Cross-domain cells are irregularly distributed in a layout.
Notes: (b) sub-mesh會佔據太多routing resource，因而導致signal routing很多DRVs
(c) sub-mesh只佔據在cross-domain cell附近
(d) 減少更多不必要的sub-mesh

## Slide 7: Introduction
Starts with a full sub-mesh with the best IR drop, and repeatedly removes unnecessary sub-meshes.
  Until the IR drop constraint cannot be satisfied.
  While the IR drop analysis in each iteration is time-consuming.
They train two models under power sub-meshes of various densities.
  IR drop prediction model
  Design rule violation prediction model
The trained models effectively guide sub-mesh construction for cross-domain cells to budget the routing resource usage on secondary power routing and signal routing.

## Slide 8: Preliminaries
Power Domain
  A collection of cells that use the same power supply during normal operation.
  Can be switched on or off at the same time.
There are numerous multiple power domain cells (cross domain cells)
  Always-on buffers/inverters, retention flip-flops, isolation cells.
  There pins called secondary power pin.
There are 2 types of power source for a cross-domain cell
  Direct supply: primary power mesh directly supplies power to the cross-domain cells.
  Indirect supply: power gating cell (MTCMOS), level shifter.

## Slide 9: Preliminaries
Static IR drop:
  Measure the weakness of the overall power delivery network.
    The average current drawn from PDN under average switching rate.
    Effective resistance from the power source to the location of interest in the layout.
Usually route power source and the secondary power pin of a cross-domain cell with wider metal than signal routing.
  Encounter more severe IR drop issue.
  Use sub-mesh reduce wire resistance and provide more via tapping location.
Notes: Set by non-default routing rule
線越寬，電阻越小

## Slide 10: Preliminaries
Input
  A timing-driven placed and clock-routed multiple power domain design.
  A set of cross-domain cells and corresponding power sources, primary power mesh and signal routing distributions.
Goal
  To construct power sub-meshes such that the IR drop constraints on cross-domain cells are satisfied.
  Design rule violations on signal routing are minimized without timing degradation.

## Slide 11: Methodology

## Slide 12: Methodology – Feature Extraction
Training layouts are generated by a multiple power domain design with different densities of sub-meshes.
The training layout is partitioned into uniform grids.
The datasets contain around 20K cross-domain cell instances
  Split them into training and validation sets with 80 : 20 split ratio.
  Perform normalization and standardization on the data feature values before the training process

## Slide 13
Extract 46 features for each target cell.
Target cell: cross-domain cell
Furthermore, in the training phase, they collect two target variables
  the static IR drop value of each cross-domain cell (with direct or indirect supply) reported by the IR drop simulation tool
  DRC hotspot grids from detailed routing

## Slide 14: Methodology – ML Model
Two datasets are adopted to train machine learning models
  IR drop percentage prediction of a given cell instance.
    is the IR drop percentage value of cell 𝑖 provided by static IR drop analysis.
  DRC hotspot prediction for the grid where the cell is located.
    indicates if there is a DRC hotspot at the grid containing cell 𝑖.

## Slide 15: Methodology – ML Model
They trained multiple regression models and output the model with the best prediction performance on the validation set.
  Extra Trees
  MLP (ANN)
  Random Forest (RF)
  XGBoost
The best model is trained by XGBoost.
Direct: IR drop on cross-domain cell with direct supply.
Indirect: IR drop on cross-domain cell with indirect supply.
DRC: DRC hotspot in a grid.
Notes: MAE: mean absolute error
RSME: root mean square error
C.C.: Correlation coefficient

## Slide 16: Methodology – ML Model

## Slide 17: Methodology – ML Model

## Slide 18: Methodology – Unit Size Selection for Sub-Meshes
The unit size of sub-mesh determines the search range for extracting features of neighboring cells.
A unit size of sub-mesh should overlap with the primary power mesh so that it can receive supply.
The unit size can contain more than one layout grid.

## Slide 19: Methodology – Unit Size Selection for Sub-Meshes
Considering a layout grid of size .
Area density of neighboring cells.
  The densities collected in each grid will be further merged as features.
Signal routing density within each layout grid.
The unit size is wider than the pitch of primary mesh
Notes: 所以sub mesh的unit size設為6*6 grid.

## Slide 20: Methodology – Model Prediction and ECO Selection

## Slide 21: Experimental Result
Implement with C++, Tcl and Python 3.7.4 (scikit-learn package) language.
Intel Xeon Linux workstation
  3.2 GHz CPU
  512 GB memory
# of direct / indirect
  Number of cross-domain cell instances with direct / indirect supply.
Training datasets: 2 power domains and 20k cross-domain cells

## Slide 22: Experimental Result
Primary power mesh is constructed on metal 10 and metal 11 layers.
Sub-meshes are on metal 8 and metal 9 layers.
IR drop constraint is 3% of the working voltage.
All the design are placed at timing optimization mode by fusion compiler.
  Timing is reported by primetime.
  IR drop analysis in done by redhawk.

## Slide 23: Experimental Result
None
  No sub-mesh
Full
  Full sub-mesh
GR-aware
  Global route congestion-aware sub-mesh
  Constructs sub-meshes only when the average layer-wise routing density is under 40%
Ours: ML
  Predicted static IR drop should be less than strictly 1%
  Zero DRC hotspots for each sub-mesh unit

## Slide 24
Notes: sub-mesh length: sub-mesh的總線長
Sub-mesh coverage%: cross-domain cell所在的grid中，sub-mesh佔的百分比
Direct IR%: 跟direct supply連接的cross-domain cell最大/平均的IR Drop的比例

## Slide 25: Experimental Result
IR drop optimization

## Slide 26: Experimental Result
Routability improvement (especially for congestion region)

## Slide 27: Experimental Result
Decreases the sub-mesh usage for cross-domain cells with direct supply.
Reserves more routing resource for the submesh of cross-domain cells with indirect supply.

## Slide 28
Thank you for listening!