## Slide 1: KOSIM: A Knowledge-oriented Derivative-free Subspace Method Based on Inexact Model for Inverse Lithography Problems
Presenter : Min-Feng Hsieh
Advisor : Ting-Chi Wang

## Slide 2: Outline
Introduction
Preliminaries
Proposed Algorithm
  Previous methods
  Barzilai-Borwein Method Enabled Nesterov Algorithm
Macro Legalization
Experimental Result

## Slide 3: Introduction
Optical lithography (光學微影技術)
  將曝光光源通過設計過的光罩，光罩上面即具有各種圖案可以阻擋或讓光穿透過去。
  若光打到正光阻上，該處會被蝕刻; 若是負光阻的話相反。
  是製造集成電路（IC）和其他半導體設備的主要工藝之一
    將微細的電子元件、晶體管、電容器等結構準確地印刷在半導體材料上

## Slide 4: Introduction
Due to the tiny scale of circuit device size, the influence of interference and diffraction will distort the image on the wafer very much.
Lots of works are proposed to resolve this kind of distortion:
  Optical proximity correction (OPC) 光學接近校正

## Slide 5: Introduction
Optical proximity correction (OPC)
  Adjust the mask layout such that the output pattern approximates the target.
  Discrete the mask into the matrix, and use the pixel-wise imaging function to characterize the imaging procedure.
  OPC process is model as an inverse problem, and is also called as inverse lithography techniques (ILT).
  Inverse problem is formulated as the non-convex optimization problem with respect to the matrix elements.
Notes: imaging procedure: 成像過程

## Slide 6: Introduction
To solve ILT:
  Approximate forward imaging modeling
    Computation of forward imaging may need numerical simulations.
    Consider the imaging function as lacking gradient, and develop general DFO method.

## Slide 7: Introduction
To solve ILT:
  Unconstraint Derivative-free optimization (DFO)
    To evaluate the efficiency of algorithm, another important index is the total number of function value evaluations (NF).
    Many model-based approached require in each iteration.
    Also need to evaluate the initialization of the model.
    Subsequence techniques are proposed to solve the large-scale DFO.

## Slide 8: Introduction
To solve ILT:
  KOSIM
    A general subspace method for solving DFO problems in ILT.
    A novel way in constructing subspaces.
    Develop a projection technique for computing an inexact gradient.
    Construct good subspaces while it only evaluates function values in each iteration.
    Only produces computational cost in each iteration.

## Slide 9: Preliminaries
Most common objective function of the ILT problem is the misfit between the image on wafer and the target pattern:
  Mask : (is discrete into matrix)
  Image function:
  Target pattern:
Optimization problem:

## Slide 10: Preliminaries
However, we will not directly accept an arbitrary solution of the above optimization problem for industry production, because of the irregularity of the corrected mask
Will do the convolution operation for times on arbitrary real matrix , which the convolution core :
Then will be truncated with the following function:
Notes: 會對U與H進行卷積，並做Nt次

## Slide 11: Preliminaries
We define the previous operation (convolution and truncation) as :
Thus the modified optimization problem becomes:
Where the matrization operator:
Notes: 會對U與H進行卷積，並做Nt次 (不是矩陣運算，所以dimension不需要對到)

## Slide 13: Algorithm
Notes: 會對U與H進行卷積，並做Nt次 (不是矩陣運算，所以dimension不需要對到)

## Slide 14
Thank you for listening!