## Slide 1: Generation of Mixed-Driving Multi-Bit Flip-Flops for Power Optimization
Meng-Yun Liu, Yu-Cheng Lai, Wai-Kei Mak, and Ting-Chi Wang
Department of Computer Science, National Tsing Hua University
Hsinchu, Taiwan

## Slide 2: Outline
Introduction
Problem Formulation
Proposed Approach
  Compute Feasible Regions of FFs
  Find All Maximal Cliques in Multiple Rectangle Intersection Graphs
  Non-Conflicting MBFFs Generation
  Location Assignment
  Timing-Driven MBFF Sizing
Experimental Result

## Slide 3: Outline
Introduction
Problem Formulation
Proposed Approach
  Compute Feasible Regions of FFs
  Find All Maximal Cliques in Multiple Rectangle Intersection Graphs
  Non-Conflicting MBFFs Generation
  Location Assignment
  Timing-Driven MBFF Sizing
Experimental Result

## Slide 4: Introduction
Clock network accounts for a major portion of power consumption in a chip
MBFFs can reduce the clock network usage, thus it is often used in low-power circuit design. The reasons are:
  The power per bit for an MBFF is smaller than a single-bit FF
  Using MBFFs reduces the number of clock sinks, resulting in less clock power consumption
    Greatly reduces the wirelength of the clock tree
    Greatly reduces the clock buffer count
Mixed-driven MBFF will have smaller area than uniform-driven MBFF

## Slide 5: Introduction
Multi-bit flip-flops (MBFFs) often used to reduce the number of clock sinks, which results in a low power design
“Traditional MBFF” is composed of individual FFs of uniform driving strength
  If some but not all of the of an MBFF violate timing constraints, the MBFF has to be sized up to a higher driving strength or decomposed into smaller bit-width combinations to satisfy timing, which reduces the power saving
This paper present a “new MBFF”, which certain bits have a higher driving strength than the other bits
  To maximize the FF merging rate, they perform aggressive FF merging subject to timing constraints
  Willing to possibly oversize some FFs, and allow the presence of empty bits in MBFF, which is for merging FFs into MBFF’s uniform driven strength as much as possible
  The oversized FF of the MBFF will be downsized subject to timing constraint with latter approach

## Slide 6: Introduction

## Slide 7: Introduction

## Slide 8: Outline
Introduction
Problem Formulation
Proposed Approach
  Compute Feasible Regions of FFs
  Find All Maximal Cliques in Multiple Rectangle Intersection Graphs
  Non-Conflicting MBFFs Generation
  Location Assignment
  Timing-Driven MBFF Sizing
Experimental Result

## Slide 9: Problem Formulation
An MBFF library containing uniform-driving and mixed-driving MBFFs, where the driving strength is from 1x to 𝑛x and the amount of bits is from 2 to 𝑘, is adopted
The Mixed-Driving MBFF Generation Problem is defined as follows:
  Input
    A netlist
    An associated legal placement
    If there are uniform-driving MBFFs in the design, they will be pre-processed by decomposing them into multiple single-bit FFs while keeping the driving strengths intact
  Output
    A refined netlist containing mixed-driving MBFFs
    A refined placement without timing violations
The objective is to minimize the amount of oversized MBFFs for power optimization, resulting in a low-power design

## Slide 10: Problem Formulation

## Slide 11: Outline
Introduction
Problem Formulation
Proposed Approach
  Compute Feasible Regions of FFs
  Find All Maximal Cliques in Multiple Rectangle Intersection Graphs
  Non-Conflicting MBFFs Generation
  Location Assignment
  Timing-Driven MBFF Sizing
Experimental Result

## Slide 12: Compute Feasible Regions of FFs
To obtain a mixed-driving MBFF design for maximum power reduction under timing constraints, the key idea is to allow upsizing of the original individual FFs to increase their merging choices when forming the MBFFs, then at the end downsizing some bits in the MBFFs formed after placement legalization while preserving timing

## Slide 13: Compute Feasible Regions of FFs
Obtain the fan-in/fan-out pin locations and their timing slacks of original FF in the design under different driving strengths
Compute the timing feasible regions of each FF under different driving strengths
The maximal cliques in each rectangle intersection graph corresponding to maximal groups of FFs that can be merged without timing violations are found to facilitate the generation of potential MBFFs

## Slide 14: Compute Feasible Regions of FFs
Obtain the fan-in/fan-out pin locations and their timing slacks of original FF in the design under different driving strengths
Compute the timing feasible regions of each FF under different driving strengths
The maximal cliques in each rectangle intersection graph corresponding to maximal groups of FFs that can be merged without timing violations are found to facilitate the generation of potential MBFFs

## Slide 15
Relocate a FF without timing violation, multiple feasible regions for each FF are computed in this stage assuming that a FF can be upsized
A timing feasible region of a FF is the intersection area of several Manhattan circles, where each Manhattan circle is centered at the fan-in/fan-out pin of the FF with its radius determined by the timing slack between the corresponding fan-in/fan-out pin and the FF
The timing slack is converted to an estimated wirelength bound by table lookup
We compute multiple feasible regions for each single-bit FF assuming
different driving strengths that are at least as large as their originally
given driving strength
The reason we consider the option of sizing up a FF is that the feasible
region of a FF is usually larger when the FF is upsized
Notes: Single bit FF A is a 2x-driving FF

## Slide 16: Compute Feasible Regions of FFs
Obtain the fan-in/fan-out pin locations and their timing slacks of original FF in the design under different driving strengths
Compute the timing feasible regions of each FF under different driving strengths
The maximal cliques in each rectangle intersection graph corresponding to maximal groups of FFs that can be merged without timing violations are found to facilitate the generation of potential MBFFs

## Slide 17
Suppose the cell library provides 1x, 2x, and 3x-driving FFs
suppose in the original netlist, FFs 𝑋, 𝑌 ,and 𝑍 are 2x-driving, 1x-driving, and 3x-driving, respectively.
So for X, we will find the 2x and 3x driven strength
So for Y, we will find the 1x, 2x and 3x driven strength
So for Z, we will find the 3x driven strength
Notes: Single bit FF A is a 2x-driving FF

## Slide 18: Compute Feasible Regions of FFs
Obtain the fan-in/fan-out pin locations and their timing slacks of original FF in the design under different driving strengths
Compute the timing feasible regions of each FF under different driving strengths
The maximal cliques in each rectangle intersection graph corresponding to maximal groups of FFs that can be merged without timing violations are found to facilitate the generation of potential MBFFs

## Slide 19
The intersections of the 𝑖x-driving feasible regions of the original FFs can be described by a rectangle intersection graph 𝐺𝑖
  Each vertex corresponds to a 𝑖x-driving feasible region of an original FF
  There is an edge between two vertices if their corresponding 𝑖x-driving feasible regions intersect
An intersection of the 𝑖x-driving feasible regions of multiple original FFs corresponds to a clique in the rectangle intersection graph 𝐺𝑖
Any set of original FFs that can form an 𝑖x-driving MBFF
without timing constraint violation must belong to some
maximal cliques in 𝐺𝑖
So we have to find all maximal cliques of sizes ≥ 2 in
each rectangle intersection graph
Notes: Single bit FF A is a 2x-driving FF

## Slide 20: Outline
Introduction
Problem Formulation
Proposed Approach
  Compute Feasible Regions of FFs
  Find All Maximal Cliques in Multiple Rectangle Intersection Graphs
  Non-Conflicting MBFFs Generation
  Location Assignment
  Timing-Driven MBFF Sizing
Experimental Result

## Slide 21: Find All Maximal Cliques in Multiple Rectangle Intersection Graphs

## Slide 22: Find All Maximal Cliques in Multiple Rectangle Intersection Graphs
Use sweep line method :
  Rotate the entire chip by 45° to make it vertical
  Then the plane is divided into a number of vertical strips by extending all vertical boundaries of the 𝑖x-driving feasible regions
  We scan each strip from top to bottom to identify the top boundaries of the rectangles called in-edges and the bottom boundaries of the rectangles called out-edges
  A clique (i.e., an intersection of multiple rectangles) is maximal within a strip if its size is greater than the clique directly above it and the clique directly below it in the same strip

## Slide 23: Outline
Introduction
Problem Formulation
Proposed Approach
  Compute Feasible Regions of FFs
  Find All Maximal Cliques in Multiple Rectangle Intersection Graphs
  Non-Conflicting MBFFs Generation
  Location Assignment
  Timing-Driven MBFF Sizing
Experimental Result

## Slide 24: Non-Conflicting MBFFs Generation
Enumerating all possible MBFF candidates for every maximal clique to find the best ones to form is extremely time-consuming, So we implement the sampling procedures called MBFF_Candidate(𝑐)
  For each maximal clique c, we randomly generate min ( C(|c|, k), 𝑆𝑎𝑚𝑝𝑙𝑒𝑏𝑜𝑢𝑛𝑑) MBFF candidates for each kind of 𝑘-bit (𝑘 ≥2) MBFFs in the library. And then selects the one with the minimum cost to be the MBFF candidate for c
  If MBFFs contain empty bit, the sampling procedure will be modified:
    k is no longer limited to the bit size, but it can be any integer ≦ min( |𝑐| , 𝑚𝑎𝑥𝑏𝑖𝑡 ) (𝑚𝑎𝑥𝑏𝑖𝑡 is the maximum bit-size in the MBFF library)
    So the algorithm can consider merging 3 FFs into a 4-bit MBFF, and 5/6/7 FFs into an 8-bit MBFF

## Slide 25: Non-Conflicting MBFFs Generation
Cost function:
  We want to form a new MBFF 𝜇 for maximum power reduction
  𝐷(𝜇) is the average merging flexibility of the FFs in 𝜇
  𝐵(𝜇) is the number of used bits in 𝜇
  𝑃𝑜𝑤𝑒𝑟(𝜇) is the FF power for 𝜇
  𝑂𝑟𝑖𝑃𝑜𝑤𝑒𝑟(𝜇) is the sum of FF powers of the original FFs that form 𝜇
  𝛼𝑖 is the switching rate of signal 𝑖
  𝑂𝑟𝑖𝑊𝐿𝑖 is the original half perimeter wirelength (HPWL) of signal 𝑖
  𝐸𝑠𝑡𝑊𝐿𝑖 is the estimated HPWL of signal 𝑖 incident with 𝜇 calculated using the estimated location for 𝜇
    Is computed by the weighted median values of the x-(y-)coordinates of all cells connected to 𝜇.
  𝜆1, 𝜆2, and 𝜆3 are user defined parameters.

## Slide 26: Non-Conflicting MBFFs Generation - Algorithm
Notes: In lines 3-4, after all of the MBFF candidates for each maximal clique are generated, they are pushed into a priority queue 𝑄 according to their costs
In line 6, Each time an MBFF candidate 𝜇 with the minimum cost in the queue is selected
In line 8-11, the FFs in 𝜇 are checked if they conflict with the MBFFs already generated in set NM𝑁𝑀
In line 12-15, 𝜇 is put into NM𝑁𝑀, and every FF in 𝜇 is marked if no conflict occurs
In line 16, the maximal clique 𝑐(𝜇) that contains 𝜇 will be reduced in size by removing all marked FFs
If the reduced clique’s size is still ≧ 2, a new MBFF candidate for it will be generated by sampling the reduced clique again and the new MBFF candidate is pushed into 𝑄 in line 17. The selection process in lines 5-18 will iterate until 𝑄 is empty

## Slide 27: Non-Conflicting MBFFs Generation - Example
Assume that an MBFF library with 1/2/4-bits MBFFs for both 1x and 2x driving is given
By performing the sweep line method, all maximal cliques with size ≥ 2 are found:
G1 has four maximal cliques:
  = {a1, b1, c1, d1}, = {e1,f1, g1}, = {i1, j1}, = {j1, k1}
G2 has four maximal cliques:
  = {a2, b2, c2, d2, e2}, = {e2, f2, g2}, = {h2, l2}, = {i2, j2, k2, m2}
After initial sampling, an MBFF candidate is found for each maximal clique
  = {a1, b1, c1, d1}, = {e1, f1, g1, - }, = {i1, j1}, = {j1, k1}
  = {a2, b2, c2, d2}, = {e2, f2, g2, - }, = {h2,l2}, = {i2, j2, k2, m2}
  Cost : < < < < < < ≤
Notes: In lines 3-4, after all of the MBFF candidates for each maximal clique are generated, they are pushed into a priority queue 𝑄 according to their costs
In line 6, Each time an MBFF candidate 𝜇 with the minimum cost in the queue is selected
In line 8-11, the FFs in 𝜇 are checked if they conflict with the MBFFs already generated in set NM𝑁𝑀
In line 12-15, 𝜇 is put into NM𝑁𝑀, and every FF in 𝜇 is marked if no conflict occurs
In line 16, the maximal clique 𝑐(𝜇) that contains 𝜇 will be reduced in size by removing all marked FFs
If the reduced clique’s size is still ≧ 2, a new MBFF candidate for it will be generated by sampling the reduced clique again and the new MBFF candidate is pushed into 𝑄 in line 17. The selection process in lines 5-18 will iterate until 𝑄 is empty

## Slide 28: Non-Conflicting MBFFs Generation – Iter. 1
In the first iteration, the minimum cost MBFF candidate is selected and put into . Then, FFs 𝑎, 𝑏, 𝑐, 𝑑 are marked. The maximal clique is updated to { }. 𝑄 becomes < < < < < ≤
Priority queue = { } -> { }
a, b, c, d is marked
= {}
Notes: In lines 3-4, after all of the MBFF candidates for each maximal clique are generated, they are pushed into a priority queue 𝑄 according to their costs
In line 6, Each time an MBFF candidate 𝜇 with the minimum cost in the queue is selected
In line 8-11, the FFs in 𝜇 are checked if they conflict with the MBFFs already generated in set NM𝑁𝑀
In line 12-15, 𝜇 is put into NM𝑁𝑀, and every FF in 𝜇 is marked if no conflict occurs
In line 16, the maximal clique 𝑐(𝜇) that contains 𝜇 will be reduced in size by removing all marked FFs
If the reduced clique’s size is still ≧ 2, a new MBFF candidate for it will be generated by sampling the reduced clique again and the new MBFF candidate is pushed into 𝑄 in line 17. The selection process in lines 5-18 will iterate until 𝑄 is empty

## Slide 29: Non-Conflicting MBFFs Generation – Iter. 2
In the second iteration, is selected and put into without conflict. Then, FFs 𝑖, 𝑗, 𝑘,𝑚 are marked. The maximal clique is updated to { }. 𝑄 becomes < < < < ≤
Priority queue = { } -> { }
a, b, c, d, i, j, k, m is marked
= {} -> {, }
Notes: In lines 3-4, after all of the MBFF candidates for each maximal clique are generated, they are pushed into a priority queue 𝑄 according to their costs
In line 6, Each time an MBFF candidate 𝜇 with the minimum cost in the queue is selected
In line 8-11, the FFs in 𝜇 are checked if they conflict with the MBFFs already generated in set NM𝑁𝑀
In line 12-15, 𝜇 is put into NM𝑁𝑀, and every FF in 𝜇 is marked if no conflict occurs
In line 16, the maximal clique 𝑐(𝜇) that contains 𝜇 will be reduced in size by removing all marked FFs
If the reduced clique’s size is still ≧ 2, a new MBFF candidate for it will be generated by sampling the reduced clique again and the new MBFF candidate is pushed into 𝑄 in line 17. The selection process in lines 5-18 will iterate until 𝑄 is empty

## Slide 30: Non-Conflicting MBFFs Generation – Iter. 3
In the third iteration, is selected and put into without conflict. Then, FFs e, f, g are marked. The maximal clique is updated to { }. 𝑄 becomes < < < ≤
Priority queue = { } -> { }
a, b, c, d, e, f, g, i, j, k, m is marked
= {} -> {, , }
Notes: In lines 3-4, after all of the MBFF candidates for each maximal clique are generated, they are pushed into a priority queue 𝑄 according to their costs
In line 6, Each time an MBFF candidate 𝜇 with the minimum cost in the queue is selected
In line 8-11, the FFs in 𝜇 are checked if they conflict with the MBFFs already generated in set NM𝑁𝑀
In line 12-15, 𝜇 is put into NM𝑁𝑀, and every FF in 𝜇 is marked if no conflict occurs
In line 16, the maximal clique 𝑐(𝜇) that contains 𝜇 will be reduced in size by removing all marked FFs
If the reduced clique’s size is still ≧ 2, a new MBFF candidate for it will be generated by sampling the reduced clique again and the new MBFF candidate is pushed into 𝑄 in line 17. The selection process in lines 5-18 will iterate until 𝑄 is empty

## Slide 31: Non-Conflicting MBFFs Generation – Iter. 4
In the forth iteration, is selected but since FFs 𝑎, 𝑏, 𝑐, 𝑑 are marked (conflict) , is discarded. Then, the maximal clique is updated to {e2} but no new MBFF candidate for needs to be generated since its size is now one(<2). 𝑄 becomes < < ≤
Priority queue = { } -> { }
a, b, c, d, e, f, g, i, j, k, m is marked
={, , } unchanged
Notes: In lines 3-4, after all of the MBFF candidates for each maximal clique are generated, they are pushed into a priority queue 𝑄 according to their costs
In line 6, Each time an MBFF candidate 𝜇 with the minimum cost in the queue is selected
In line 8-11, the FFs in 𝜇 are checked if they conflict with the MBFFs already generated in set NM𝑁𝑀
In line 12-15, 𝜇 is put into NM𝑁𝑀, and every FF in 𝜇 is marked if no conflict occurs
In line 16, the maximal clique 𝑐(𝜇) that contains 𝜇 will be reduced in size by removing all marked FFs
If the reduced clique’s size is still ≧ 2, a new MBFF candidate for it will be generated by sampling the reduced clique again and the new MBFF candidate is pushed into 𝑄 in line 17. The selection process in lines 5-18 will iterate until 𝑄 is empty

## Slide 32: Non-Conflicting MBFFs Generation – Iter. 5
In the fifth iteration, is selected and put into without conflict. Then, FFs ℎ,𝑙 are marked. The maximal clique is updated to { }. 𝑄 becomes < ≤
Priority queue = { } -> { }
a, b, c, d, e, f, g, h, i, j, k, l, m is marked
={, , } -> {, , , }
Notes: In lines 3-4, after all of the MBFF candidates for each maximal clique are generated, they are pushed into a priority queue 𝑄 according to their costs
In line 6, Each time an MBFF candidate 𝜇 with the minimum cost in the queue is selected
In line 8-11, the FFs in 𝜇 are checked if they conflict with the MBFFs already generated in set NM𝑁𝑀
In line 12-15, 𝜇 is put into NM𝑁𝑀, and every FF in 𝜇 is marked if no conflict occurs
In line 16, the maximal clique 𝑐(𝜇) that contains 𝜇 will be reduced in size by removing all marked FFs
If the reduced clique’s size is still ≧ 2, a new MBFF candidate for it will be generated by sampling the reduced clique again and the new MBFF candidate is pushed into 𝑄 in line 17. The selection process in lines 5-18 will iterate until 𝑄 is empty

## Slide 33: Non-Conflicting MBFFs Generation – finish
In the remaining iterations, the rest of the MBFF candidates in 𝑄 all contain some marked FFs thus conflict with those MBFFs in 𝑁𝑀 . When 𝑄 becomes empty, the algorithm terminates.
Priority queue = { } -> {}
a, b, c, d, e, f, g, h, i, j, k, l, m is marked
={, , , } not changed
Notes: In lines 3-4, after all of the MBFF candidates for each maximal clique are generated, they are pushed into a priority queue 𝑄 according to their costs
In line 6, Each time an MBFF candidate 𝜇 with the minimum cost in the queue is selected
In line 8-11, the FFs in 𝜇 are checked if they conflict with the MBFFs already generated in set NM𝑁𝑀
In line 12-15, 𝜇 is put into NM𝑁𝑀, and every FF in 𝜇 is marked if no conflict occurs
In line 16, the maximal clique 𝑐(𝜇) that contains 𝜇 will be reduced in size by removing all marked FFs
If the reduced clique’s size is still ≧ 2, a new MBFF candidate for it will be generated by sampling the reduced clique again and the new MBFF candidate is pushed into 𝑄 in line 17. The selection process in lines 5-18 will iterate until 𝑄 is empty

## Slide 34: Non-Conflicting MBFFs Generation – summary
So the final MBFFs formed in the non-conflicting set 𝑁𝑀 are:
  = {a1, b1, c1, d1}
  = {e1, f1, g1, - } with an empty bit
  = {h2,l2}
  = {i2, j2, k2, m2}
Notes: In lines 3-4, after all of the MBFF candidates for each maximal clique are generated, they are pushed into a priority queue 𝑄 according to their costs
In line 6, Each time an MBFF candidate 𝜇 with the minimum cost in the queue is selected
In line 8-11, the FFs in 𝜇 are checked if they conflict with the MBFFs already generated in set NM𝑁𝑀
In line 12-15, 𝜇 is put into NM𝑁𝑀, and every FF in 𝜇 is marked if no conflict occurs
In line 16, the maximal clique 𝑐(𝜇) that contains 𝜇 will be reduced in size by removing all marked FFs
If the reduced clique’s size is still ≧ 2, a new MBFF candidate for it will be generated by sampling the reduced clique again and the new MBFF candidate is pushed into 𝑄 in line 17. The selection process in lines 5-18 will iterate until 𝑄 is empty

## Slide 35: Outline
Introduction
Problem Formulation
Proposed Approach
  Compute Feasible Regions of FFs
  Find All Maximal Cliques in Multiple Rectangle Intersection Graphs
  Non-Conflicting MBFFs Generation
  Location Assignment
  Timing-Driven MBFF Sizing
Experimental Result

## Slide 36: Location Assignment
To minimize the WL of the signal nets incident with the MBFFs, each MBFF in the non-conflicting set is assigned to an initial location within its preferred region
The weight of a pin is the switching rate of the signal net between the MBFF and the pin
First, the weighted median interval of the x-(y-) coordinates of MBFF’s fan-in and fan-out pins are calculated
Then, the preferred region is formed by the intersection of these two weighted median intervals (X-axis and Y-axis)

## Slide 37: Location Assignment
The bins covered by the preferred region of an MBFF are called its preferred bins
  The rank of the preferred bins of an MBFF is set to 0
  Increasing ranks are given to other bins within the feasible region of an MBFF7 according to their distance from its preferred bins
  Each MBFF is assigned to the vacant slot that is closest to the preferred region within the lowest-ranked bin inside its feasible region
  The slot size is set to the size of 2x-driving 2-bit MBFF in the experiment
  This is to ensure that there will be a minimal overlap of the MBFFs with other cells so that any overlap can be resolved using a commercial tool with little disturbance to the original placement in order to preserve timing.

## Slide 38: Outline
Introduction
Problem Formulation
Proposed Approach
  Compute Feasible Regions of FFs
  Find All Maximal Cliques in Multiple Rectangle Intersection Graphs
  Non-Conflicting MBFFs Generation
  Location Assignment
  Timing-Driven MBFF Sizing
Experimental Result

## Slide 39: Timing-driven MBFF Sizing
After the location assignment is completed, the netlist and placement are updated and saved as DEF and Verilog files by commercial tool
Placement legalization and timing analysis will then be done by a commercial tool
So far all bits in the same MBFF have identical driving strength
After timing analysis, we will try to downsize some bits of an MBFF if possible to save more power while maintaining zero negative slack.
Without loss of generality, we assume that a mixed-driving MBFF mixes two driving strengths, low and high. Given an MBFF where all bits have high driving strength initially, we try to replace it with a mixed-driving MBFF having low and high driving strengths as shown in Algorithm 2

## Slide 40: Timing-driven MBFF Sizing

## Slide 41: Outline
Introduction
Problem Formulation
Proposed Approach
  Compute Feasible Regions of FFs
  Find All Maximal Cliques in Multiple Rectangle Intersection Graphs
  Non-Conflicting MBFFs Generation
  Location Assignment
  Timing-Driven MBFF Sizing
Experimental Result

## Slide 42
Thank You for Listening!