## Slide 1: PUFFER :A Routability-Driven Placement Framework via Cell Padding.pdf
Yao-Wen Chang
Department of Electrical Engineering
National Taiwan University, Taipei 10617, Taiwan
Zhijie Cai, Peng Zou, Xingyu Tong, Jun Yu, Jianli Chen
State Key Lab of ASIC & System
Fudan University, Shanghai 200433, China
Zhengtao Wu
Shanghai LEDA Technology Co., Ltd.,
Shanghai 201203, China
Presenter : Min-Feng Hsieh
Adviser : Ting-Chi Wang

## Slide 2: Outline
Abstract
Introduction
Preliminaries
Proposed Algorithm
Experimental Result
Conclusion

## Slide 3: Outline
Abstract
Introduction
Preliminaries
Proposed Partitioning Framework For Multi-GPU Acceleration
Experimental Result
Conclusion

## Slide 4: Abstract
Estimate the congestion by imitating routing detour and clustered cell spreading.
Use the method of cell padding and strategy exploration for optimizing routibility during global placement and legalization stage.
Cell padding considers multiple features, which accumulating accurate congestion.
Apply Bayesian-based method to avoid parameter tuning.
PUFFER achieves best routability with 2.7x(commercial) and 1.4x(Replace) speedups.
Notes: Placement is critical for the routability optimization.

## Slide 5: Outline
Abstract
Introduction
Preliminaries
Proposed Partitioning Framework For Multi-GPU Acceleration
Experimental Result
Conclusion

## Slide 6: Introduction
Routability-driven placement typically consists of:
  Basic placement engine: Quadratic placement, non-linear placement.
  Routability optimizer.
Notes: In quadratic placement, an iterative framework with lower and upper bounds is often applied. The lower bound is described by a quadratic wirelength model to minimize wirelength, and the upper bound is generated by spreading cells in high density regions to remove cell overlaps
In non-linear placement, the objective function is formulated by a non-linear wirelength model subject to a density constraint. By relaxing the density constraint into the objective function, the placement problem can be solved by gradient-descent-based methods to obtain a high-quality placement solution with the desired tradeoff between wirelength and cell density.

## Slide 7: Preliminaries
Routability-driven Placement Problem
H= (V, E), where V= ,E= .
The placement solution= (x, y)= , where () is the coordinate of .

## Slide 8: Preliminaries
We can formulate analytical global routing problem as:
wirelength.
Density penalty to spread cells.
λ : Density penalty factor
Notes: Λ : to balance the weight between wirelength and density
After doing global routing, we need to legalize the cell positions to remove cell overlaps
and DRC violations.

## Slide 9: Preliminaries
Electrostatic-based Placement
This model adopts the weighted-average(WA) wirelength model to approximate the HPWL.
= -
Notes: Electrostatic: 靜電
weighted wirelength of net ei
Γ: smoothing parameter used to adjust the accuracy.
Electrostatic: 靜電
𝑊_(𝑒_𝑖 ) (𝑥, 𝑦): weighted wirelength of net ei
Γ: smoothing parameter used to adjust the accuracy.

## Slide 10: Preliminaries
To get the density penalty, the placement region will first divide into uniform bins by M×M grids.
: area of cell I
: the bin in row m and column n
) : the electric potential of

## Slide 11: Preliminaries
Global routing congestion
Use the Gcell-based routing resource model, which evaluates the routing capacity and demand with respect to the Gcell.
=
: the routing demands of Gcell g
: the routing capacity of Gcell g
Notes: Electrostatic: 靜電
weighted wirelength of net ei
Γ: smoothing parameter used to adjust the accuracy.
Electrostatic: 靜電
𝑊_(𝑒_𝑖 ) (𝑥, 𝑦): weighted wirelength of net ei
Γ: smoothing parameter used to adjust the accuracy.

## Slide 12: Proposed Algorithm

## Slide 13
Thank you for listening!