## Slide 1: Fast STA Graph Partitioning Framework for Multi-GPU Acceleration
Tsung-Wei Huang
Department of Electrical and Computer Engineering
University of Utah, Salt Lake City, UT, USA
Guannan Guo
Department of Electrical and Computer Engineering
University of Illinois at Urbana-Champaign, IL, USA
Martin Wong
Department of Computer Science and Engineering
The Chinese University of Hong Kong, Shatin, NT, Hong Kong

## Slide 2: Outline
Abstract
Introduction
Proposed Partitioning Framework For Multi-GPU Acceleration

## Slide 3: Abstract
Path-based Analysis (PBA) is a key process in Static Timing Analysis (STA) to reduce excessive slack pessimism (Graph Based Analysis, GBA).
However, PBA can easily become the major performance bottleneck due to its long execution time.
To overcome this bottleneck, recent STA researches have proposed to accelerate PBA algorithms with manycore CPU and GPU parallelisms.
In this work, we introduce a new, fast endpoint-oriented partitioning framework that can separate STA graphs and dispatch the PBA workload onto multiple GPUs.
Notes: However, GPU memory is rather limited when we compute PBA on large industrial designs with millions of gates. So a natural solution is to partition the circuit graph to reduce space complexity

## Slide 4: Introduction
This framework can quickly process the STA graph and build an end-point graph, which reflects the size of shared logic between endpoints
  It takes linear time to construct an endpoint graph.
  Endpoints with larger shared logic are grouped together in the same partition, which allows us to propagate shared timing information in a single partition.
  If there exists shared logic across different partitions, we make minimal duplications to ensure we can conduct independent analysis.
Then they will separate the endpoint graph into groups and recover the partitions
  Use the method of METIS graph partitioning
  Recover the full partitions by a linear recovery process

## Slide 5: Introduction
Also with GPU manager, they can accelerate the PBA process on multiple GPUs
  We associate one CPU core to monitor the execution status of one GPU device
  We also leverage the work-stealing scheduler to move the imbalance analysis

## Slide 6: Proposed Partitioning Framework For Multi-GPU Acceleration
Step 1. Rank Circuit Pins
  Process the circuit graph by ranking the circuit pins based on their distances from the source pins

## Slide 7: Proposed Partitioning Framework For Multi-GPU Acceleration
Step 2. Build Endpoint Graph
  The endpoint graph can reflect the size of common logic between endpoints

## Slide 8: Proposed Partitioning Framework For Multi-GPU Acceleration
Step 3. Find Disjoint Endpoint Sets
  Based on the endpoint graph, we identify independent components, which is represented by a set of endpoints

## Slide 9: Proposed Partitioning Framework For Multi-GPU Acceleration
Step 4. Determine whether the sets are balanced
  If the size of these disjoint sets are balanced, we can just pack them together
  If the size of these disjoint sets are unbalanced, they will use the method of METIS graph partition to separate the endpoint graph

## Slide 10: Proposed Partitioning Framework For Multi-GPU Acceleration
Step 5. Partition Graph Recovery
  Use the method of linear BFS algorithm
  Leverage a multithread library, Taskflow, to offload and monitor the PBA workloads of all partitions on multiple GPU devices

## Slide 11: Proposed Partitioning Framework For Multi-GPU Acceleration – STA Graph Model
Model the circuit graph as a DAG (used in lots of STA engine)
  Vertex: circuit pin
  Edge: pin-to-pin connection
Endpoint: the endpoint of a datapath (FF input, PO, …)
Graph representation : Compressed Sparse Row (CSR)
  Commonly used as a condensed graph format in GPU applications
  Can avoid cost of conversion
To save fan-in STA graph and fan-out STA graph which allow us to search in both directions
Notes: CSR format contain three linear array, which holds:
  Vertex offset
  Edge destinations
  Edge weights

## Slide 12: Proposed Partitioning Framework For Multi-GPU Acceleration – Circuit Pin Ranking
To estimate the size of shared logic, we use the minimum distance of each vertex to the source pins, denoted as .